## Slide 1
DIGITAL DESIGN & COMPUTER ARCHITECTURE
Combinational Logic & Sequential Logic
Building the ALU · Registers · Counters · FSMs
DDCA Group 13 · Module 2 + Module 3
INPUTS
bits
COMBINATIONAL
ALU
SEQUENTIAL
state
CPU
next instruction
Samhitha
2620090087
Mithil
2620090108
Sampath
2620090101
Hemanth
2620090109

## Slide 2
ROADMAP
What We'll Cover
DDCA · Group 13 · Modules 2 & 3
2
1
COMBINATIONAL LOGIC
No memory · current inputs
2
ARITHMETIC CIRCUITS
Add · subtract · compare
3
THE ALU
One calculator block for the CPU
4
SEQUENTIAL LOGIC
State · clock · flip-flops
5
REGISTERS + FSMs
Remember · step · control
One thread connects both modules: combinational logic computes a result; sequential logic stores it and moves the CPU forward.

## Slide 3
MODULE 2
Making Decisions with Combinational Logic
DDCA · Group 13 · Modules 2 & 3
3
DEFINING IDEA
Output depends only on the current inputs. No memory. No clock. No stored state.
INPUTS
A, B, C
LOGIC
gates
OUTPUT
Y
K-MAPS
Simplify Boolean expressions by grouping adjacent 1s (or 0s). Fewer terms → fewer gates → faster, cheaper, lower-power hardware.
Example: 2-variable K-map
0
1
1
1
→ grouped terms → simplified logic
Worked examples keep the design flow concrete: specification → truth table → K-map → simplified circuit.

## Slide 4
MODULE 2
Arithmetic Circuits: From Bits to Wide Adders
DDCA · Group 13 · Modules 2 & 3
4
HALF ADDER
A + B
SUM = A ⊕ B CARRY = A · B
FULL ADDER
A + B + Cᵢₙ
SUM = A ⊕ B ⊕ Cᵢₙ Cₒᵤₜ generated by logic
RIPPLE-CARRY ADDER
FA0
FA1
FA2
FA3
Carry ripples from the least-significant bit toward the most-significant bit.
SUBTRACTION WITH TWO'S COMPLEMENT
A − B = A + (~B) + 1
One control bit can choose add or subtract: invert B when SUB = 1, and feed SUB into the carry-in.
ADD/SUB CONTROL
SUB = 0 → A + B SUB = 1 → A + ~B + 1
Wide adders are slower because carry information must travel across stages.

## Slide 5
MODULE 2
The ALU: The CPU's Calculator
DDCA · Group 13 · Modules 2 & 3
5
STANDARD BLOCKS
Multiplexer — selects one data path
Decoder — activates one output line
Comparator — equality / ordering tests
ALU
A
B
ADD
SUB
AND
OR
SLT
OP SELECT
Operation-select input chooses what the ALU computes.
RESULT
MILESTONE
Working ALU in the simulator

## Slide 6
MODULE 2
Specification → Circuit → Simulation
DDCA · Group 13 · Modules 2 & 3
6
1
SPECIFY
What must the circuit do?
2
TRUTH TABLE
Enumerate input / output behaviour
3
SIMPLIFY
Use Boolean algebra / K-map
4
BUILD
Choose gates and connect them
5
TEST
Verify every important case
SIMULATOR CHECK
A
0
B
0
SUB
1
OP
0
→
ALU
→
RESULT = verified
Milestone: a working ALU is the first major sub-system of the RISC-V CPU.

## Slide 7
PROJECT SUMMARY
From Logic to a Living CPU
1
COMBINATIONAL
Logic computes from current inputs.
2
ALU
Add, subtract, AND, OR and compare in one block.
3
SEQUENTIAL
Flip-flops and clocks give the machine state.
4
CPU FABRIC
Registers, PC and FSMs remember and step.
Small, testable blocks combine into the first major pieces of a RISC-V CPU.
THANK YOU