## Slide 1
DIGITAL DESIGN & COMPUTER ARCHITECTURE
Combinational Logic & Sequential Logic
Building the ALU · Registers · Counters · FSMs
DDCA Group 13 · Module 2 + Module 3
INPUTS
bits
COMBINATIONAL
ALU
SEQUENTIAL
state
CPU
next instruction
Samhitha
2620090087
Mithil
2620090108
Sampath
2620090101
Hemanth
2620090109

## Slide 2
MODULE 3
Remembering & Keeping Time: Sequential Logic
DDCA · Group 13 · Modules 2 & 3
7
WHY STATE?
Combinational logic forgets. A CPU must remember values and step through instructions one clock at a time.
STATE
NEXT STATE
feedback
LATCHES & FLIP-FLOPS
SR LATCH
set / reset
D LATCH
level-sensitive
D FLIP-FLOP
edge-triggered
CLOCK
Edge-triggering makes synchronous systems predictable. Setup/hold time matters around the active clock edge.

## Slide 3
MODULE 3
Registers & Counters: Giving the CPU a Memory
DDCA · Group 13 · Modules 2 & 3
8
REGISTER
0
1
0
1
0
1
0
1
8 flip-flops → one 8-bit stored value
SHIFT REGISTER
1
2
3
4
Bits move left or right each clock.
PROGRAM-COUNTER PATTERN
00
01
10
11
The PC stores 'which instruction is next'. A clock edge updates the stored address.
CLOCK EDGE
register captures
old value
→
new value
Synchronous design: all storage elements respond to the same clock discipline.

## Slide 4
MODULE 3
Finite State Machines: Turning Steps into Hardware
DDCA · Group 13 · Modules 2 & 3
9
A FSM describes step-by-step behaviour using states + transitions. The control unit can be built from this pattern.
IDLE
RUN
DONE
WAIT
start
done
reset
wait
STATE TABLE
IDLE
start → RUN
RUN
done → DONE
DONE
reset → IDLE
WAIT
resume → RUN
FSM DESIGN FLOW
specification → states → transitions → flip-flops + logic → simulate
Milestone: a small controller working in the simulator demonstrates the CPU's memory-and-stepping fabric.

## Slide 5
PROJECT SUMMARY
From Logic to a Living CPU
1
COMBINATIONAL
Logic computes from current inputs.
2
ALU
Add, subtract, AND, OR and compare in one block.
3
SEQUENTIAL
Flip-flops and clocks give the machine state.
4
CPU FABRIC
Registers, PC and FSMs remember and step.
Small, testable blocks combine into the first major pieces of a RISC-V CPU.
THANK YOU